Interior Design II Objective 5.02		Date __________	Period _____	Name ____________________

Furniture Clearances for Traffic Patterns
Traffic patterns are based on major furniture pieces. They should be convenient and direct, not waste space, and avoid cutting through the middle of rooms or interrupting activities.

Living Spaces: living & family rooms, den & study

1. Major traffic pattern: 2-4 ft. 
 
2. Path between low objects: (for example, between sofa and table) = 1 ft. 6 in.

3. Foot space between chair and low table: 1 ft.

Notes: conversation area = 10 ft. diameter. TV viewing angle 45 degrees

Dining Room

1. Serving path & chair space: 3-4 ft.

2. Table width per person: 2 ft.

Additional Dimensions & Clearances

- Closet depth: clothes closet 2 ft.; entry closet 2 ft. 3 in.

- Stair width: 3 ft.; secondary stair can be 2 ft. minimum (check with your building code)

- Hallway width: 3 ft.; 3 ft. 6 in. at entry

- Garage:

  - one car 10 ft. by 20 ft. (12 ft. by 22 ft. preferred)

  - two car 20 ft. by 20 ft. (22 ft. by 24 ft. preferred)

- Piano bench to wall: 3 ft.

# Text boxes

Bathroom

- WC wall to counter top or bathtub: 5’6”

- Bathtub to countertop: 24” - 36”

- Sink width: 2 ft. 6 in.

- Toilet width: 2 ft. 6 in.

Kitchen

- Total length of work triangle = 22 ft.

- Distance between parallel counters = 3 ft. 6 in – 4 ft.

- Work Areas: 1 ft. 6 in. – 2 ft. on each side

- To open appliance doors: 3 ft. 6 in. in front

Bedroom

- Dressing area in front of closet and chest of drawers:  3-4 ft.

Note: minimum size 9 ft. by 9 ft. = for one twin bed (10 ft. by 10 ft. preferred minimum)